## Slide 1: HDMI Exploitation

## Slide 2: Agenda
HDMI CEC?
Exploiting HDMI
Applications
Exploiting PS5 by HDMI

## Slide 3: HDMI CEC?

## Slide 4
HDMI Consumer Electronics Control (CEC) is a protocol built into HDMI connections that allows multiple devices connected through HDMI cables to communicate with and control each other.
It enables actions such as turning on a TV and having it automatically switch to the correct input when a game console or Blu-ray player is powered on, or controlling playback and volume using a single remote.
CEC works by sending control commands through a dedicated wire within the HDMI cable, allowing up to 15 devices to share control instructions over the same connection.
Although the feature is standardized under the HDMI specification, manufacturers often market it under brand-specific names like Anynet+ for Samsung, Bravia Sync for Sony, and Simplink for LG.
HDMI CEC simplifies home entertainment setups by reducing the number of remotes needed and automating device interactions, creating a more seamless user experience.
📺 What is HDMI CEC?

## Slide 6: Exploiting HDMI!

## Slide 7: Exploiting HDMI?
AS any other technology HDMI CEC can be abused, that because HDMIC CEC can go beyond just running a device on and of or raising the volume level!
In some devices like PS5 and other media devices, you can use this feature to completely control the device using your TV remote!
The complete control of a device can lead to unexpected automated control. Since devices like PS5 has no official way to automatically control them, inappropriate security measures can be found.
How controlling a device using a TV remote can lead to automatic control?

## Slide 8: TV API

## Slide 9: TV API
As mentioned earlier media devices like PS5 does not have an official way to control them programmatically. However, TVs like Samsung TVs usually have an API server hosted on the tv, this API server can be used to control the TV using a TCP connection instead of infra red.
This feature is useful when you lose your TV remote, as it can help you controlling the TV using your phone and an application. The issue occurs when there is no rate limit to limit the number of the TCP Segments.
If a device support HDMI-CEC is connected to a TV that can be programmatically controlled, then we can programmatically control this device using the TV and the HDMI cable as a bridge! This can be exploited to break things like PINS!

## Slide 10: Applications

## Slide 11: Applications
  Bypassing weak security measures
  Games cheating
  Can help you finding other bugs

## Slide 12: Exploiting PS5!

## Slide 13: PS5 As an example
The idea for this exploration began with an interest in remotely controlling the PS5 programmatically. Initial attempts to use PS5 controller protocols were met with limitations, as they were not designed for this use case. The breakthrough came from observing the use of a Samsung Smart TV remote to control the PS5 via HDMI-CEC, which allowed us to explore control using Samsung's APIs.
The discovery that a Samsung Smart TV remote could control the PS5 inspired the idea of programmatically controlling the TV to indirectly manage the PS5. Research into Samsung's Smart TV APIs revealed existing libraries and user contributions, which were refined and adapted for this purpose.

## Slide 14: The code
  During this project we have developed a code that is both user friendly and effective. The code is completely written in python and works for both Linux and windows! And it can automate the whole process. The main purpose of this code is to crack any local account by guessing the PIN.
  Key features:
  1- automatic TV discovery by utilizing python-nmap module
  2- saves the API token of the TV, so users do not need to request every time
  3- you can specify the password range
  4- user friendly CLI and good documentation

## Slide 15: Demo of the CLI

## Slide 16: Demo video

## Slide 17: Thank you